## Slide 3: Land use of the Yazoo River Basin
Image: MDEQ (2008)
Total area: 13,510 mi2
41% cropland
30% forested
12% wetland
10% pasture
4% urban
3% water
30% of land area in state
20% of state population
Parajuli and Kim (2012)
...wood in the streams and bayous of the Yazoo-Mississippi Delta was extensive before large-scale deforestation occurred.
Bryant (2010)
Flood Control Reservoirs:
Arkabutla (1943): 1,000 mi2 drainage
Sardis (1940): 1,545 mi2 drainage
Enid (1952): 560 mi2 drainage
Grenada (1954):1,320 mi2 drainage

## Slide 4
Ten-mile Bayou in Delta National Forest Bryant (2010)
Historically, the Yazoo delta plain was heavily forested in riparian areas
Tree growth and frequent flooding resulted in uneven micro-topographic features (1-3 meters in elevation)
Extensive canebrakes along natural levees – possibly at the site of pre-European agricultural disturbances
Log-jams from stream-side forests were common throughout Delta Plain
Large-scale logging and removal of log-jams occurred by late 1800s
Forested LULC and log-jam evidence dates back to Hernando DeSoto’s explorations (1541)

## Slide 5: Ecoregions of the Yazoo River Basin
Image: Parajuli and Kim (2012)
73 – Mississippi Alluvial Plain
73a – Northern Holocene Meander Belts
73b – Northern Pleistocene Valley Trains
73d – Northern Backswamps
74 - Mississippi Valley Loess Plains
74a – Bluff Hills
74b – Loess Plains
65 – Southeastern Plains
65b – Flatwoods/Blackland Prairie Margins
65d – Southern Hilly Gulf Coastal Prairie
65e – Northern Hilly Gulf Coastal Prairie
Image: USEPA (2018)

## Slide 6: Water Quality Concerns
Image: MDEQ (2006)
Pollutants include: organic and nutrient enrichment from animal wastes and failing septic systems, bacteria from those same sources, and sediment from eroding lands (pasture, timber operations, new development).
- MDEQ (2006)
Chart: Of monitored streams in Bluff Hills:
| Good/Very Good | Fair | Poor/Very Poor
Stream ratings | 23 | 36 | 41
“Adequately support” aquatic life
“Somewhat impacted” aquatic life
“Significantly impacted” aquatic life

## Slide 7: Water Quality Concerns and Impact on Fisheries
Image: MDEQ (2006)
Of 134 fish species found in the portion of the Lower Mississippi Alluvial Valley within the state, 102 species can be found in the Yazoo Delta Plain
Paddlefish and sturgeon found in Yazoo and Sunflower tributaries to the Mississippi River
Sport fish (bluegills, sunfish, largemouth bass, crappies) are found in the oxbow lakes of the Delta Plain
Turbidity of waters may prevent some species from being more prevalent
Bryant (2010)
Toxicity sampling has been conducted and resulted in fish advisories for the Delta Plain
Limit consumption of: carp, buffalo, gar, and large catfish
Okay to consume: bass, bream, crappie, freshwater drum, small (or farm-raised) catfish
Waters within Mississippi River levees are okay
MDEQ (2010)

## Slide 8: Yazoo River Basin Watershed Assessment
Eric White | Tulane University | RCSE-6840 | April 25, 2012
Problem Statement/Research Question
To what extent do the four flood control reservoirs in the Bluff Hills impact seasonality of water flows and nutrients of concern in the Yazoo River Basin?
All four reservoirs are located in the Bluff Hills, which have very different land use/agricultural practices than the Delta Plain. These disparate systems experience the same climatology; therefore, can a paired watershed approach be designed to assess relative differences between a variety of mitigation/restoration techniques?

## Slide 9: Flow data coverage in the Bluff Hills basins

## Slide 10: Flow data coverage in the Bluff Hills basins

## Slide 11: Flow data coverage in the Delta Plain basins

## Slide 12
Flow for sites with no dams upstream – Bluff Hills

## Slide 13
Flow for sites with no dams upstream – Bluff Hills

## Slide 14
Flow for sites with no dams upstream – Delta Plain

## Slide 15
Flow for sites with a dam upstream – Bluff Hills

## Slide 16
Flow for sites with a dam upstream – Delta Plain

## Slide 17
Flow for sites with a dam upstream – Delta Plain

## Slide 18: Water Temperature
Map shows all sites (including wells) – only surface water samples were included in this analysis.

## Slide 19: Total Kjeldahl Nitrogen
1L.O.C. = 0.69 mg/L
1L.O.C. = 0.69 mg/L
2L.O.C. = 0.3 – 0.36 mg/L
2L.O.C. = 0.3 – 0.36 mg/L
1US EPA (2001)
2US EPA (2000)
Map shows all sites (including wells) – only surface water samples were included in this analysis.

## Slide 20: Challenges & Improvement Observations
Regardless of location with Yazoo basin, TKN concentrations are at or above levels of concern
Reservoir controls have clear impacts on seasonality of flows
Temperature may not be largely impacted by reservoir controls
TKN concentrations appear to have less seasonality downstream of dams
Entire Delta Plain (aside from the Yazoo mainstem) does not have dams

## Slide 21: Challenges & Improvement Observations
This system can essentially be set up as a suite of paired watersheds
  Test landuse/topographic/geologic differences (n = 6)
    Sunflower basin vs five basins in Bluff Hills above dams
  Test impact of dams/reservoir operations (n=4)
    Upstream and downstream
History of data collection is rich
  A thorough statistical design could be set up to examine these impacts over the past 50-60 years (post dam construction in the 1940s)
  Will have less ability to do this analysis on data sets that need to be flow-weigthed (not many coupled flow-constituent timeseries)
The need for improvement is high – many impaired streams
  Can use the paired watershed approach to test mitigation/restoration options

## Slide 22: References
Bryant, M.D. (2010). Past and Present Aquatic Habitats and Fish Populations of the Yazoo-Mississippi Delta. General Technical Report SRS-130. USDA Forest Service – Southern Research Section. Stoneville, MS.
De Cicco, L.A. and Hirsch, R.M. (2014). The dataRetrieval R package. United States Geological Survey.
Flowers, J.C. (2016). Images of America: Clarksdale and Coahoma County. Carnegie Public Library. Arcadia Publishing.
Mississippi Department of Environmental Quality. (2006). Citizen’s Guide to Water Quality in the Yazoo Basin.
Parajuli, P.B. and Kim, H. (2012). Yazoo River Basin Assessment: Preliminary Report. Bulletin 1202. Mississippi State University, Mississippi Agricultural & Forestry Experiment Station.
U.S. Environmental Protection Agency. (2000). Ambient Water Quality Criteria Recommendations Information Supporting the Development of State and Tribal Nutrient Criteria Rivers and Streams in Nutrient Ecoregion IX. U.S. EPA Office of Water. https://www.epa.gov/sites/production/files/documents/rivers9.pdf
U.S. Environmental Protection Agency. (2001). Ambient Water Quality Criteria Recommendations Information Supporting the Development of State and Tribal Nutrient Criteria Rivers and Streams in Nutrient Ecoregion X. U.S. EPA Office of Water. https://www.epa.gov/sites/production/files/documents/rivers10.pdf
U.S. Environmental Protection Agency. (2013). Level III and IV ecoregions of the continental United States. Corvallis, Oregon, U.S. EPA National Health and Environmental Effects Research Laboratory. https://www.epa.gov/eco-research/level-iii-and-iv-ecoregions-continental-united-states.